## Slide 1: CSE 205: Digital Logic Design
Dr. Tanzima Hashem
Professor
CSE, BUET

## Slide 2: Textbook
Digital Design (5th Edition)
  M. Morris Mano
  Michael D. Ciletti

## Slide 3: Digital Systems
Digital Systems
  Example: digital cameras, digital telephones, digital television, digital computers…
  Used in communication, business transactions, traffic control, space guidance, medical treatment, weather monitoring, the Internet …
Why study digital logic design
  To design and build a digital system

## Slide 4: Boolean (Binary) Logic
Deals with binary variables and binary logic functions
Binary variables has two discrete values
  0, False, Open
  1, True, Close
Three basic logical operations
  AND (.); OR (+); NOT (‘)

## Slide 5: Truth Table
Specifies results for all possible input combinations

## Slide 6: Logic Gates
Logic gates are electronic circuits that operate on one or more input signals to produce an output signal

## Slide 7: Boolean Function
An algebraic expression
  Binary variables
  Constants 0 and 1
  Logic operation symbols
f(x,y,z) = (x + y’)z + x’
Some terminology, notation and precedence:
  f is the name of the function.
  (x,y,z) are the input variables, each representing 1 or 0.
  A literal is a single variable within a term, in complemented or uncomplemented form. The function above has four literals: x, y’, z, and x’.
  Parenthesis has the highest precedence, followed by NOT, AND, and then OR.

## Slide 8: Boolean Function
A Boolean function can be represented in a truth table.
f(0,0,0) = (0 + 1)0 + 1 = 1
f(0,0,1) = (0 + 1)1 + 1 = 1
f(0,1,0) = (0 + 0)0 + 1 = 1
f(0,1,1) = (0 + 0)1 + 1 = 1
f(1,0,0) = (1 + 1)0 + 0 = 0
f(1,0,1) = (1 + 1)1 + 0 = 1
f(1,1,0) = (1 + 0)0 + 0 = 0
f(1,1,1) = (1 + 0)1 + 0 = 1
f(x,y,z) = (x + y’)z + x’

## Slide 9: Gate Implementation of a Function

## Slide 10: Gate Implementation of a Function

## Slide 11: Boolean Algebra
Algebra for binary values
  Boolean Algebra: Developed by George Boole in 1854
Why study Boolean Algebra?
  To find the simplest circuit implementation with the smallest number of gates or wires
  Simpler circuits are cheaper to build, consume less power, and run faster than complex circuits

## Slide 12: Algebra
What is an algebra?
  Mathematical system consisting of
    Set of elements
    Set of operators
    Axioms or postulates: facts that can be taken as true; they do not require proof

## Slide 13: Axiomatic definition of Boolean Algebra
A Boolean algebra requires
  A set of elements B, consisting of two elements (0 and 1)
  Two binary operations OR and AND
  The axioms below must always be true

## Slide 14: Axiomatic definition of Boolean Algebra
Based on axiom #5, we can develop a unary (one-argument) operation NOT

## Slide 15: Axiomatic definition of Boolean Algebra
The distributive laws
x | y | z | y+z | x．(y+z) | x．y | x．z | (x．y)+(x．z)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 16: Duality principle
If an expression is valid in Boolean algebra, the dual of that expression is also valid
To form the dual of an expression, replace
  all + operators with . operators,
  all . operators with + operators,
  all ones with zeros, and
  all zeros with ones
Form the dual of the expression
  a + (bc) = (a + b)(a + c)
Following the replacement rules…
  a(b + c) = ab + ac

## Slide 17: Duality principle
The left and right columns of axioms are duals
  exchange all ANDs with ORs, and 0s with 1s

## Slide 18: Basic theorems of Boolean Algebra
In addition to the axioms, additional laws can be derived; they are called theorems of Boolean Algebra
These theorems are useful in performing algebraic manipulations of Boolean expressions

## Slide 19: Proof of x+x=x
We can only use Huntington postulates:
Show that x+x=x.
  x+x = (x+x)·1 by 2(b)
  = (x+x)(x+x’) by 5(a)
  = x+xx’ by 4(b)
  = x+0 by 5(b)
  = x by 2(a)
We can now use Theorem 1(a) in future proofs
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0

## Slide 20: Proof of x·x=x
Similar to previous proof
Show that x·x = x.
  x·x = xx+0 by 2(a)
  = xx+xx’ by 5(b)
  = x(x+x’) by 4(a)
  = x·1 by 5(a)
  = x by 2(b)
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 1: (a) x+x=x

## Slide 21: Proof of x+1=1
Theorem 2(a): x + 1 = 1
x + 1 = 1．(x + 1) by 2(b)
  =(x + x')(x + 1) 5(a)
  = x + x' 1 4(b)
  = x + x' 2(b)
  = 1
Theorem 2(b): x．0 = 0 by duality
Theorem 4: (x')' = x
  Postulate 5 defines the complement of x, x + x' = 1 and x x' = 0
  The complement of x' is x is also (x')'
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 1: (a) x+x=x, (b) x.x =x

## Slide 22: Absorption Property (Covering)
Theorem 6(a): x + xy = x
x + xy = x．1 + xy by 2(b)
= x (1 + y) 4(a)
= x (y + 1) 3(a)
= x．1 Th 2(a)
= x 2(b)
Theorem 6(b): x (x + y) = x by duality
By means of truth table (another way to proof )
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 1: (a) x+x=x, (b) x.x =x
Th. 2: (a) x + 1 = 1, (b) x.0 =0

## Slide 23: Absorption Property (Covering)
Theorem 6(a): x + xy = x
x | y | xy | x+xy
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 1

## Slide 24: DeMorgan’s Theorem
Theorem 5(a): (x + y)’ = x’y’
Theorem 5(b): (xy)’ = x’ + y’
By means of truth table
x | y | x’ | y’ | x+y | (x+y)’ | x’y’ | xy | x’+y' | (xy)’
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0

## Slide 25: Consensus Theorem
xy + x’z + yz = xy + x’z
(x+y)•(x’+z)•(y+z) = (x+y)•(x’+z) -- (dual)
Proof: xy + x’z + yz = xy + x’z + (x+x’)yz = xy + x’z + xyz + x’yz = (xy + xyz) + (x’z + x’zy)
= xy(1+z) + x’z (1+y) = xy + x’z

## Slide 26: Gate Implementation of a Function
F2=x’y’z + x’yz + xy’ = x’z(y’+y) + xy’ = x’z +xy’

## Slide 27: Gate Implementation of a Function

## Slide 28: Practice
Simplify the following Boolean expressions to a minimum number of literals:
  xyz + x'y + xyz’
  (A + B)'(A' + B') '
xyz + x'y + xyz' = xy(z + z') + x'y = xy + x'y = y
(A + B)'(A' + B')' = (A'B')(A B) = 0

## Slide 29: Complement of a Function
Applying DeMorgan’s theorems:
f(x,y,z) = x(y’z’ + yz)
f ’(x,y,z) = (x(y’z’ + yz))’ [ complement both sides ]
= x’ + (y’z’ + yz)’ [ because (xy)’ = x’ + y’ ]
= x’ + (y’z’)’ (yz)’ [ because (x + y)’ = x’ y’ ]
= x’ + (y + z)(y’ + z’) [ because (xy)’ = x’ + y’, twice]

## Slide 30: Complement of a Function
The complement of a function always outputs 0 where the original function outputted 1, and 1 where the original produced 0
f(x,y,z) = (x + y’)z + x’

## Slide 31: Complement of a Function
By taking the dual of f and complementing each literal:
  If f(x,y,z) = x(y’z’ + yz)…
  …the dual of f is x + (y’ + z’)(y + z)…
  …then complementing each literal gives
  x’ + (y + z)(y’ + z’)…
  …so f’(x,y,z) = x’ + (y + z)(y’ + z’)

## Slide 32: Practice
Find the complement of the following expressions:
  xy' + x'y
  [(x' + y + z')(x + y')(x + z)]
F' = (xy' + x'y)'
= (xy')'(x'y)'
= (x' + y)(x + y')
= xy + x'y‘
F' = [(x' + y + z')(x + y')(x + z)]'
= (x' + y + z')' + (x + y')' + (x + z)'
= xy'z + x'y + x'z'

## Slide 33: Generalized DeMorgan’s Theorem
(A + B + C)’ = (A + x)’ let B + C = x
= A’x’
= A’ (B + C)’
= A’ (B’C’)
= A’B’C’
Complement of a function is obtained
  Interchanging AND and OR operators
  Complementing each literal

## Slide 34: Minterms
A minterm is an AND term in which every variable or its complement occurs once
  F(x,y) has 4 minterms x’y’, x’y, xy’, xy
An n variable function has 2n valid minterms
A minterm equals 1 at exactly one input combination and is equal to 0 otherwise
  Example: x’y’z’ = 1 only when x=0, y=0, z=0

## Slide 35: Maxterms
A maxterm is an OR term in which every variable or its complement occurs once
  F(x,y) has 4 maxterms x’+y’, x’+y, x+y’, x+y
An n variable function has 2n valid maxterms
A maxterm equals 0 at exactly one input combination and is equal to 1 otherwise
  Example: (x+y+z) = 0 only when x=0, y=0, z=0

## Slide 36: Example: Three Binary Variables

## Slide 37: Canonical Form
Any boolean function that is expressed as a sum of minterms or as a product of maxterms is said to be in its canonical form.

## Slide 38: Sum of Minterms
F1(x, y, z) = ∑(1,4,5,6,7) = m1 + m4 + m5 + m6 + m7
      =x' y' z + xy' z’ + xy' z + xyz’ + xyz

## Slide 39: Sum of Minterms: Example
F = x + yz
= x(y + y’)(z + z’) + (x + x’)yz = xyz + xyz’ + xy’z + xy’z’ + xyz + x’yz = x’yz + xy’z’ + xy’z + xyz’ + xyz = (3,4,5,6,7)
Or convert the expression into truth-table and then read the minterms from the table

## Slide 40: Product of Maxterms
A Boolean function can be expressed algebraically from a given truth table
  by forming a maxterm for each combination of the variables that produces a 0 in the function, and
  then taking the AND of all those maxterms.

## Slide 41: Product of Maxterms
F1(x, y, z) = ∏(0,2,3) = M0 ×M2 ×M3
= (x + y + z)(x + y'+z)(x + y'+z')

## Slide 42: Product of Maxterms: Example
F = xy + x’z = (xy+x’)(xy+z)
  = (x+x’)(y+x’)(x+z)(y+z) = (x’+y)(x+z)(y+z)
  x’+y = x’+y+zz’ = (x’+y+z)(x’+y+z’)
  x+z = x+z+yy’ = (x+y+z)(x+y’+z)
  y+z = y+z+xx ’ = (x+y+z)(x ’+y+z)
  F =(x+y+z)(x+y’+z)(x’+y+z)(x’+y+z’)
    =M0M2M4M5= ∏(0, 2, 4,5)
Or convert the expression into truth-table and then read the maxterms from the table

## Slide 43: Conversion between Canonical Forms
Conversion between minterms and maxterms
m0 = x’y’z’ = (x+y+z)’ = (M0)’
  In general, mi = (Mi)’
Sum of minterms  Product of maxterms:
  f = (0,1,2,3,6)
  f’= (4,5,7) = m4 + m5 + m7
  (f’)’= (m4 + m5 + m7)’
  f = m4’ m5’ m7’ [DeMorgan’s law]
  = M4 M5 M7 = ∏(4,5,7)

## Slide 44: Conversion between Canonical Forms
In general, to convert from one canonical form to another, interchange the symbols  and ∏ and list those numbers missing from the original form.
  Example: f = (0,1,2,3,6) = ∏(4,5,7)

## Slide 45: Practice
Express the following function (four variables: A, B, C, D) as a sum of minterms and as a product of maxterms:
  F = B'D + A'D + BD
F = ∑(1, 3, 5, 7, 9, 11,13, 15)
= ∏(0, 2, 4, 6, 8, 10, 12, 14)

## Slide 46: Standard Form
Any boolean function that is expressed as a sum of products (SOP) or as a product of sums (POS), where each product-term or sum-term may contain one, two, or any number of variables, is said to be in its standard form.
SOP: f(x,y,z) = xy + x’yz + xy’z
POS: f(x,y,z) = (x’ + y’)(x + y’ + z’)(x’ + y + z’)

## Slide 47: Non-Standard and Standard Forms

## Slide 48: Practice
Convert the following expression into sum of products and product of sums:
  (AB + C)(B + C'D)
(AB + C)(B + C'D)
= AB + BC + ABC'D + CC'D
= AB(1 + C'D) + BC
= AB + BC (SOP form)
= B(A + C) (POS form)

## Slide 49: Canonical and Standard Forms
Canonical forms
  Sum of minterms (SOM)
  Product of maxterms (POM)
Standard forms (may use less gates)
  Sum of products (SOP)
  Product of sums (POS)
F = ab+a’ (already sum of products:SOP)
F = ab + a’(b+b’) (expanding term)
F = ab + a’b + a’b’ (it is canonical form:SOM)

## Slide 50: Other Logic Operations
2n rows in the truth table of n binary variables.
22^n functions for n binary variables.
16 functions of two binary variables.

## Slide 51: Boolean Expressions

## Slide 52: Digital Logic Gates
Boolean expression: AND, OR and NOT operations
Constructing gates of other logic operations
  The feasibility and economy;
  The possibility of extending gate's inputs;
  The basic properties of the binary operations (commutative and associative);
  The ability of the gate to implement Boolean functions.

## Slide 53: Summary of Logic Gates
Figure 2.5 Digital logic gates

## Slide 54
Figure 2.5 Digital logic gates
Summary of Logic Gates

## Slide 55: Multiple Inputs
Extension to multiple inputs
  A gate can be extended to multiple inputs.
    If its binary operation is commutative and associative.
  AND and OR are commutative and associative.
    OR
      x+y = y+x
      (x+y)+z = x+(y+z) = x+y+z
    AND
      xy = yx
      (x y)z = x(y z) = x y z

## Slide 56: Multiple Inputs
NAND and NOR are commutative but not associative → they are not extendable.

## Slide 57: Multiple Inputs
Multiple NOR = a complement of OR gate, Multiple NAND = a complement of AND.
The cascaded NAND operations = sum of products.
The cascaded NOR operations = product of sums.

## Slide 58: Multiple Inputs
The XOR and XNOR gates are commutative and associative.
Multiple-input XOR gates are uncommon
XOR is an odd function: it is equal to 1 if the inputs variables have an odd number of 1's.

## Slide 59: Positive and Negative Logic
Positive and Negative Logic
  Two signal values <=> two logic values
  Positive logic: H=1; L=0
  Negative logic: H=0; L=1

## Slide 60: Syllabus
Chapter 2 (Excluding Section 2.9)