## Slide 1: CSE 205: Digital Logic Design
Dr. Tanzima Hashem
Professor
CSE, BUET

## Slide 2: Logic Circuits
Logic Circuits: Combinational and Sequential
Combinational Circuits
  A combinational circuit consists of logic gates whose outputs at any time are determined from only the present combination of inputs
Sequential Circuits
  A sequential circuits employ storage elements and logic gates
  The outputs are a function of the inputs and the state of the storage elements.
  The state of the storage elements, in turn, is a function of the previous inputs (and the previous state)

## Slide 3: Combinational Circuits
The n input binary variables come from an external source.
The m output variables are produced by the internal combinational logic circuit and go to an external destination.

## Slide 4: Combinational Circuits
?
?
?
Analysis
  Given a circuit, find out its function
  Function may be expressed as:
    Boolean function
    Truth table
Design
  Given a desired function, determine its circuit
  Function may be expressed as:
    Boolean function
    Truth table

## Slide 5: Analysis Procedure Boolean Expression Approach
F2 = AB + AC + BC
T1 = A + B + C
T2 = ABC
T3 = F2´ T1
F1 = T3 + T2
Or
F1 = A´BC´ + A´B´C + AB´C´ + ABC

## Slide 6: Analysis Procedure Truth Table Approach
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1
F2
0
0
0
1
0
1
1
1
F2 ´
1
1
1
0
1
0
0
0
T3
0
1
1
0
1
0
0
0
T2
0
0
0
0
0
0
0
1
T1
0
1
1
1
1
1
1
1
F1
0
1
1
0
1
0
0
1

## Slide 7: Design Procedure
4-bits
0-9 values
4-bits
Value+3
?
Given a problem statement:
  Determine the number of inputs and outputs
  Derive the truth table
  Simplify the Boolean expression for each output
  Produce the required circuit and verify it
Example:
Design a circuit to convert a “BCD” code to “Excess 3” code

## Slide 8: Design Procedure BCD-to-Excess 3 Converter
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
 |  |  |  | C |  |  | 
 |  |  | 1 | 1 | 1 | B | 
A |  | x | x | x | x |  | 
 |  | 1 | 1 | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  | 1 |  |  |  | B | 
A |  | x | x | x | x |  | 
 |  |  | 1 | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  | 1 |  | 1 |  |  | 
 |  | 1 |  | 1 |  | B | 
A |  | x | x | x | x |  | 
 |  | 1 |  | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  | 1 |  |  | 1 |  | 
 |  | 1 |  |  | 1 | B | 
A |  | x | x | x | x |  | 
 |  | 1 |  | x | x |  | 
 |  |  | D |  |  |  | 
w = A+BC+BD
x = B’C+B’D+BC’D’
y = C’D’+CD
z = D’

## Slide 9: Design Procedure BCD-to-Excess 3 Converter
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
w = A + B(C+D)
x = B’(C+D) + B(C+D)’
y = (C+D)’ + CD
z = D’

## Slide 10: Binary Adder
The most basic arithmetic operation is the addition of two binary digits.
A combinational circuit that performs the addition of two bits is half adder
A adder performs the addition of 2 significant bits and a previous carry is called a full adder

## Slide 11: Binary Adder
HA
x
y
S
C
x y | C S
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
x
+ y
───
C S
x
y
S
C
Half Adder
  Adds 1-bit plus 1-bit
  Produces Sum and Carry

## Slide 12: Binary Adder
x y z | C S
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
x
+ y
+ z
───
C S
FA
x
y
z
S
C
 |  |  |  | y | 
 |  | 0 | 1 | 0 | 1
x |  | 1 | 0 | 1 | 0
 |  |  | z |  | 
 |  |  |  | y | 
 |  | 0 | 0 | 1 | 0
x |  | 0 | 1 | 1 | 1
 |  |  | z |  | 
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz
Full Adder
  Adds 1-bit plus 1-bit plus 1-bit
  Produces Sum and Carry

## Slide 13: Binary Adder
Full Adder
x
y
z
S
C
x
y
z
S
C
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz

## Slide 14: Binary Adder
x
y
z
S
C
HA
x
y
z
HA
S
C
Full Adder
S = x  y  z
C = (x  y)z + xy
x
y
z
S
C
C = (x  y)z + xy

## Slide 15: Binary Adder
  c3 c2 c1 .
  + x3 x2 x1 x0
  + y3 y2 y1 y0
  ────────
Cy S3 S2 S1 S0
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Binary Adder
x3x2x1x0 y3y2y1y0
S3S2S1S0
C0
Cy
Carry Propagate Addition

## Slide 16: Four-Bit Binary Adder
Carry bits must “ripple” through each stage of a multi-bit adder before the output settles down to the correct result.
Significantly slower --> Rippling effect of carry
For an n bit adder, Propagation delay = (Number of gate level x Average gate delay) x (number of bits)

## Slide 17: Carry Lookahead Logic
Carry Propagate Pi = Ai ⊕ Bi
Carry Generate Gi = Ai Bi
Si = Pi ⊕ Ci
Ci+1 = Gi + Ci Pi

## Slide 18: Carry Lookahead Logic
All carries can be generated simultaneously
  C2 = G1 + P1C1
  C3 = G2 + P2C2 = G2 + P2G1 + P2P1C1
  C4 = G3 + P3C3 = G3 + P3G2 + P3P2G1 + P3 P2P1C1

## Slide 19: Carry Lookahead Logic

## Slide 20: 4-Bit Adder with Carry Lookahead

## Slide 21: Binary Subtractor
Half Subtractor
  Produces x -y
  D – difference
D = x’y +xy’ = S of half adder
B = x’y
HS
x
y
B
D
x y | B D
0 0 | 0 0
0 1 | 1 1
1 0 | 0 1
1 1 | 0 0
x
- y
───
B D

## Slide 22: Binary Adder
Full Subtractor
  (x -y) –z; where z represents a borrow
x y z | B D
0 0 0 | 0 0
0 0 1 | 1 1
0 1 0 | 1 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 0 0
1 1 0 | 0 0
1 1 1 | 1 1
FS
x
y
z
D
B
 |  |  |  | y | 
 |  | 0 | 1 | 0 | 1
x |  | 1 | 0 | 1 | 0
 |  |  | z |  | 
 |  |  |  | y | 
 |  | 0 | 1 | 1 | 1
x |  | 0 | 0 | 1 | 0
 |  |  | z |  | 
D = xy'z'+x'yz'+x'y'z+xyz = x  y  z
B= x'y + x'z + yz

## Slide 23: Binary Subtractor
Use 2’s complement with binary adder
  x – y = x + (-y) = x + y’ + 1

## Slide 24: Binary Adder/Subtractor
M: Control Signal (Mode)
  M=0  F = x + y
  M=1  F = x – y

## Slide 25: Overflow
An overflow occurs when two number of n digits each are added and the sum occupies n+1 digits
When two unsigned numbers are added, an overflow is detected from the end carry out of the most significant position
When two signed numbers are added, the sign bit is treated as part of the number and the end carry does not indicate an overflow
  Extra overflow detection circuits are required
An overflow can only occur when two numbers added are both positive or both negative

## Slide 26: Overflow

## Slide 27: Overflow
INPUTS |  |  | OUTPUTS |  | 
Asign | Bsign | CARRY IN | CARRY OUT | SUMsign | OVERFLOW
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0

## Slide 28: Overflow
Unsigned Binary Numbers
2’s Complement Numbers
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Carry
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Overflow

## Slide 29: Decimal Adder
A decimal adder requires a minimum of 9 inputs
and 5 outputs
  1 digit requires 4-bit
  Input: 2 digits + 1-bit carry
  Output: 1 digit + 1-bit carry
BCD adder
  Perform the addition of two decimal digits in BCD, together with an input carry from a previous stage
  The output sum cannot be greater than 19 (9+9+1)

## Slide 30: BCD Adder
4-bits plus 4-bits
Operands and Result: 0 to 9
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0
X +Y | x3 x2 x1 x0 | y3 y2 y1 y0 | Sum | Cy | S3 S2 S1 S0
0 + 0 | 0 0 0 0 | 0 0 0 0 | = 0 | 0 | 0 0 0 0
0 + 1 | 0 0 0 0 | 0 0 0 1 | = 1 | 0 | 0 0 0 1
0 + 2 | 0 0 0 0 | 0 0 1 0 | = 2 | 0 | 0 0 1 0
0 + 9 | 0 0 0 0 | 1 0 0 1 | = 9 | 0 | 1 0 0 1
1 + 0 | 0 0 0 1 | 0 0 0 0 | = 1 | 0 | 0 0 0 1
1 + 1 | 0 0 0 1 | 0 0 0 1 | = 2 | 0 | 0 0 1 0
1 + 8 | 0 0 0 1 | 1 0 0 0 | = 9 | 0 | 1 0 0 1
1 + 9 | 0 0 0 1 | 1 0 0 1 | = A | 0 | 1 0 1 0
2 + 0 | 0 0 1 0 | 0 0 0 0 | = 2 | 0 | 0 0 1 0
9 + 9 | 1 0 0 1 | 1 0 0 1 | = 12 | 1 | 0 0 1 0
Invalid Code
Wrong BCD Value
0001 1000

## Slide 31: BCD Adder
X +Y | x3 x2 x1 x0 | y3 y2 y1 y0 | Sum | Cy | S3 S2 S1 S0 | Required BCD Output | Value
9 + 0 | 1 0 0 1 | 0 0 0 0 | = 9 | 0 | 1 0 0 1 | 0 0 0 0 1 0 0 1 | = 9
9 + 1 | 1 0 0 1 | 0 0 0 1 | = 10 | 0 | 1 0 1 0 | 0 0 0 1 0 0 0 0 | = 16
9 + 2 | 1 0 0 1 | 0 0 1 0 | = 11 | 0 | 1 0 1 1 | 0 0 0 1 0 0 0 1 | = 17
9 + 3 | 1 0 0 1 | 0 0 1 1 | = 12 | 0 | 1 1 0 0 | 0 0 0 1 0 0 1 0 | = 18
9 + 4 | 1 0 0 1 | 0 1 0 0 | = 13 | 0 | 1 1 0 1 | 0 0 0 1 0 0 1 1 | = 19
9 + 5 | 1 0 0 1 | 0 1 0 1 | = 14 | 0 | 1 1 1 0 | 0 0 0 1 0 1 0 0 | = 20
9 + 6 | 1 0 0 1 | 0 1 1 0 | = 15 | 0 | 1 1 1 1 | 0 0 0 1 0 1 0 1 | = 21
9 + 7 | 1 0 0 1 | 0 1 1 1 | = 16 | 1 | 0 0 0 0 | 0 0 0 1 0 1 1 0 | = 22
9 + 8 | 1 0 0 1 | 1 0 0 0 | = 17 | 1 | 0 0 0 1 | 0 0 0 1 0 1 1 1 | = 23
9 + 9 | 1 0 0 1 | 1 0 0 1 | = 18 | 1 | 0 0 1 0 | 0 0 0 1 1 0 0 0 | = 24
+ 6










## Slide 32: BCD Adder
Correct Binary Adder’s Output (+6)
  If the result is between ‘A’ and ‘F’
  If Cy = 1
S3 S2 S1 S0 | Err
0 0 0 0 | 0
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 1
1 0 1 1 | 1
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
 |  |  |  | S1 |  |  | 
 |  |  |  |  |  | S2 | 
S3 |  | 1 | 1 | 1 | 1 |  | 
 |  |  |  | 1 | 1 |  | 
 |  |  | S0 |  |  |  | 
Err = S3 S2 + S3 S1

## Slide 33: BCD Adder
Err

## Slide 34: Binary Multipilier

## Slide 35: Binary Multipilier

## Slide 36: Magnitude Comparator
Magnitude Comparator
A3A2A1A0 B3B2B1B0
A<B A=B A>B
Compare 4-bit number to 4-bit number
  3 Outputs: < , = , >
  Expandable to more number of bits

## Slide 37: Magnitude Comparator

## Slide 38: Decoders
A decoder is a combinational circuit that converts binary information from n input lines to an 2n unique output lines.
1-to-2-Line Decoder

## Slide 39: Decoders
Binary Decoder
x1
x0
Only one lamp will turn on
0
0
1
0
0
0
1
0
2
3
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number

## Slide 40: Decoders
2-to-4 Line Decoder
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 0 0 0 1
0 1 | 0 0 1 0
1 0 | 0 1 0 0
1 1 | 1 0 0 0
Binary Decoder
I1
I0
Y3
Y2
Y1
Y0

## Slide 41: Decoders
Binary Decoder
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
3-to-8 Line Decoder

## Slide 42: Decoders
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 0 0 0 1
0 1 | 0 0 1 0
1 0 | 0 1 0 0
1 1 | 1 0 0 0
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 1 1 1 0
0 1 | 1 1 0 1
1 0 | 1 0 1 1
1 1 | 0 1 1 1
Binary Decoder
I1
I0
Y3
Y2
Y1
Y0
Binary Decoder
I1
I0
Y3
Y2
Y1
Y0
Active-High / Active-Low

## Slide 43: Decoders
“Enable” Control
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
E | I1 I0 | Y3 Y2 Y1 Y0
0 | x x | 0 0 0 0
1 | 0 0 | 0 0 0 1
1 | 0 1 | 0 0 1 0
1 | 1 0 | 0 1 0 0
1 | 1 1 | 1 0 0 0

## Slide 44: Decoders

## Slide 45: Decoders
I2 I1 I0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0
Y7
Y6
Y5
Y4
Y3
Y2
Y1
Y0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0
Expansion
I2 I1 I0 | Y7 Y6 Y5 Y4 Y3 Y2 Y1 Y0
0 0 0 | 0 0 0 0 0 0 0 1
0 0 1 | 0 0 0 0 0 0 1 0
0 1 0 | 0 0 0 0 0 1 0 0
0 1 1 | 0 0 0 0 1 0 0 0
1 0 0 | 0 0 0 1 0 0 0 0
1 0 1 | 0 0 1 0 0 0 0 0
1 1 0 | 0 1 0 0 0 0 0 0
1 1 1 | 1 0 0 0 0 0 0 0

## Slide 46: Implementation Using Decoders
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Decoder
x
y
z
S C
Each output is a minterm
All minterms are produced
Sum the required minterms
  Example: Full Adder
  S(x, y, z) = ∑(1, 2, 4, 7)
  C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 47: Implementation Using Decoders
F(x, y, z) = ∑(3, 5, 6, 7)
Active High Decoder, OR gate
SOP

## Slide 48: Implementation Using Decoders
F(x, y, z) = ∑(3, 5, 6, 7)
Active High Decoder, NOR gate
SOP->POS
F(x, y, z) = ∏(0, 1, 2, 4)

## Slide 49: Implementation Using Decoders
F(x, y, z) = ∑(3, 5, 6, 7)
Active Low Decoder, NAND gate
SOP

## Slide 50: Implementation Using Decoders
F(x, y, z) = ∑(3, 5, 6, 7)
Active Low Decoder, AND gate
SOP->POS
F(x, y, z) = ∏(0, 1, 2, 4)

## Slide 51: Encoders
Does reverse operation to decoder
An encoder has 2n (or fewer) input lines and n output lines
Constraint – only one input is active at a time

## Slide 52: Encoders
I7 I6 I5 I4 I3 I2 I1 I0 | Y2 Y1 Y0
0 0 0 0 0 0 0 1 | 0 0 0
0 0 0 0 0 0 1 0 | 0 0 1
0 0 0 0 0 1 0 0 | 0 1 0
0 0 0 0 1 0 0 0 | 0 1 1
0 0 0 1 0 0 0 0 | 1 0 0
0 0 1 0 0 0 0 0 | 1 0 1
0 1 0 0 0 0 0 0 | 1 1 0
1 0 0 0 0 0 0 0 | 1 1 1
Binary Encoder
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0
Octal-to-Binary Encoder (8-to-3)

## Slide 53: Priority Encoders
Encoder with priority function
  Multiple inputs may be true simultaneously
  Higher priority input gets the precedence

## Slide 54: Priority Encoders
Priority Encoder
V
Y1
Y0
I3
I2
I1
I0
4-Input Priority Encoder
I3 I2 I1 I0 | Y1 Y0 | V
0 0 0 0 | x x | 0
0 0 0 1 | 0 0 | 1
0 0 1 x | 0 1 | 1
0 1 x x | 1 0 | 1
1 x x x | 1 1 | 1

## Slide 55: Multiplexers
A multiplexer is a combinational circuit that selects one of many input lines (2n) and directs it to its single output line.
There are n selection lines whose bit combinations determine which input is selected.

## Slide 56: Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
4-to-1 MUX
S1 S0 | Y
0 0 | I0
0 1 | I1
1 0 | I2
1 1 | I3

## Slide 57: Multiplexers
S1 S0 | Y
0 0 | I0
0 1 | I1
1 0 | I2
1 1 | I3
X
Y
MUX
F
I0
I1
I2
I3
S1 S0
Z
Z
0
1

## Slide 58: Multiplexers
Quad 2-to-1 MUX
MUX
Y
I0
I1
S
MUX
Y
I0
I1
S
MUX
Y
I0
I1
S
MUX
Y
I0
I1
S
A3
A2
A1
A0
B3
B2
B1
B0
S
MUX
A3
A2
A1
A0
S E
Y3
Y2
Y1
Y0
B3
B2
B1
B0

## Slide 59: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
x y | F
0 0 | 1
0 1 | 1
1 0 | 0
1 1 | 1
x y
F
1
1
0
1
Example F(x, y) = ∑(0, 1, 3)

## Slide 60: Implementation Using Multiplexers
x y z | F
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 0
1 0 1 | 0
1 1 0 | 1
1 1 1 | 1
MUX
Y
I0
I1
I2
I3 I4
I5
I6
I7
S2 S1 S0
x y z
0
1
1
0
0
0
1
1
F
Example F(x, y, z) = ∑(1, 2, 6, 7)

## Slide 61: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
x y z | F
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 0
1 0 1 | 0
1 1 0 | 1
1 1 1 | 1
x y
F
F = z
z
F = z
z
F = 0
0
F = 1
1
F(x, y, z) = ∑(1, 2, 6, 7)

## Slide 62: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3 I4
I5
I6
I7
S2 S1 S0
A B C D | F
0 0 0 0 | 0
0 0 0 1 | 1
0 0 1 0 | 0
0 0 1 1 | 1
0 1 0 0 | 1
0 1 0 1 | 0
0 1 1 0 | 0
0 1 1 1 | 0
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 0
1 0 1 1 | 1
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
A B C
F
F = D
D
F = D
D
F = D
D
F = 0
0
F = 0
F = D
F = 1
F = 1
0
D
1
1
F(A, B, C, D) = ∑(1, 3, 4, 11, 12, 13, 14, 15)

## Slide 63: Implementation Using Multiplexers
Steps:
  Complete the truth table from the SOP.
  The first n – 1 variables in the table are applied to the selection inputs of the multiplexer.
  For each combination of the selection variables, we evaluate the output as a function of the last variable.
  Apply these values to the data input in proper order.

## Slide 64: Multiplexer Expansion 8-to-1 MUX using Dual 4-to-1 MUX
Y
I0
I1
I2
I3
I4
I5
I6
I7
S2 S1 S0
MUX
Y
I0
I1
I2
I3
S1 S0
MUX
Y
I0
I1
I2
I3
S1 S0
MUX
Y
I0
I1
S
0 0
1

## Slide 65: DeMultiplexers
A decoder with enable input can function as a demultiplexer – a circuit receives information from a single line and directs it to one of 2n possible output lines.

## Slide 66: DeMultiplexers / Decoders
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
E | I1 I0 | Y3 Y2 Y1 Y0
0 | x x | 0 0 0 0
1 | 0 0 | 0 0 0 1
1 | 0 1 | 0 0 1 0
1 | 1 0 | 0 1 0 0
1 | 1 1 | 1 0 0 0
DeMUX
I
Y3
Y2
Y1
Y0
S1 S0

## Slide 67: Demultiplexers
E | I1 I0 | Y3 Y2 Y1 Y0
0 | x x | 0 0 0 0
1 | 0 0 | 0 0 0 1
1 | 0 1 | 0 0 1 0
1 | 1 0 | 0 1 0 0
1 | 1 1 | 1 0 0 0

## Slide 68: Three-State Gates
A
Y
C
C A | Y
0 x | Hi-Z
1 0 | 0
1 1 | 1
A
Y
C
Tri-State Buffer
Tri-State Inverter

## Slide 69: Three-State Gates 2-to-1-line mux
Y=
A
C
B
A if C = 1
B if C = 0

## Slide 70: Three-State Gates 4-to-1-line mux
I0
Y
E
S1
I1
I2
I3
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
S0

## Slide 71: Practice
Using a decoder and external gates, design the combinational circuit defined by the following three boolean functions:
F1 = x’ y’z’ + xz = ∑ (0, 5, 7)
F2 = xy’z’ + x’y = ∑ (2, 3, 4)
F3 = x’y’z + xy = ∑ (1, 6, 7)

## Slide 72: Practice
A combinational circuit is specified by the following three boolean functions:
F1 (A, B, C) = ∑ (2, 4, 7)
F2 (A, B, C) = ∑ (0, 3)
F3 (A, B, C) = ∑ (0, 2, 3, 4, 7)
Implement the circuit with a decoder constructed with NAND gates.

## Slide 73: Practice
Implement the following Boolean function with a 4 X 1 multiplexer and external gates.
F(A, B, C, D) = ∑ (1, 3, 4, 11, 12, 1 3, 14, 15)

## Slide 74: Practice
Implement the following Boole an function with a 4 X 1 multiplexer and external gates.
F(A, B, C, D) = ∑ (1, 2, 4, 7, 8, 9, 10, 11, 13, 15)

## Slide 75: Practice
Construct a 16 X 1 multiplexer with two 8 X 1 and one 2 X 1 multiplexers. Use block diagrams

## Slide 76: Practice
Using four half-adders design a 4-bit combinational circuit incrementer (a circuit that adds 1 to a 4-bit binary number)

## Slide 77: Practice
Using a half-adder and three full-adeders design a 4-bit combinational circuit decrementer (a circuit that subtracts 1 from a 4-bit binary number)

## Slide 78: Practice
Design a combinational circuit that compares two 4-bit numbers to check if they are equal. The circuit output is equal to 1 if two numbers are equal and 0 otherwise.