## Slide 1: CSE 205: Digital Logic Design
Dr. Tanzima Hashem
Professor
CSE, BUET

## Slide 2: Programmable Logic Arrays (PLAs)
Pre-fabricated building block of many AND/OR gates
An array of programmable AND gates
  can generate any product terms of the inputs
An array of programmable OR gates
  can generate the sums of the products

## Slide 3: Programmable Logic Arrays (PLAs)
Before programming, all possible connections available before "programming“
”Personalized" by making or breaking connections among gates

## Slide 4: PLA Example
Example: AND/OR/XOR
  F1 = AB′ + AC + A′BC′
  F2 = (AC + BC)′
XOR gates can invert the outputs
  invert: connected to 1
  not change: connected to 0
PLA programming table: 3 sections
  1. list the product terms
  2. specify the required paths between inputs and AND gates
  3. specify the paths between the AND and OR gates

## Slide 5: Programmable Logic Arrays (PLAs)
Size of PLA: specified by # of inputs, product terms and outputs
  n inputs, k product terms and m outputs
  n buffer-inverter gates, k AND gates, m OR gates, and m XOR gates
Designing a digital system with a PLA
  reduce the number of distinct product terms
  the number of literals in a product is not important

## Slide 6: Implement with PLAs
F1(A, B, C) = Σ (0, 1, 2, 4); F2(A, B, C) = Σ (0, 5, 6, 7)
Simply both the true and complement of the functions in sum of products
Find the combination with minimum number of product terms
  F1=(AB+AC+BC)’
  F2=AB+AC+A’B’C’
Obtain the PLA programming table

## Slide 7: Syllabus
Chapter 7:7.6